## Slide 1: Geospatial 101
Doing stuff in python

## Slide 2: Introduction to Geospatial Data
Projections
Vector Data
Raster Data

## Slide 3: What are projections?
A projection is a method for representing the 3D surface of the earth on a 2D map.
Projections are a compromise, each one minimizes different types of distortion (distance, shape, area)
Different projections are used depending on the purpose of the map/analysis, and the accuracy required.

## Slide 4: Different Projections
https://www.axismaps.com/guide/map-projections
WGS84 | Lambert Azimuthal Equal Area
WGS84 | Mercator
WGS84 | UTM 10 N

## Slide 5: Datums: What’s the WGS84 thing?
Projections are a method for distorting the 3D earth into a 2D map. A datum is how we define the coordinate system. (I think kinda like choosing the best place to project from that minimizes error across the map)
Satellites and Surveyors go around and measure reference points on the earth and take into account the shape, tectonic movements, etc.
Different datums optimized for different regions.
  WGS84 – global
  NAD83 – North America
  ETRF - Europe

## Slide 6: How important is this?
Are you a surveyor?
  Probably very
Otherwise
  Probably not
  It’s important to know it exists
  Transform your dataset into the right projection system (CRS) and then forget about it
  I just use NAD83 | UTM 10 N for here
    (is that the right thing to do? I dunno, works for me)

## Slide 7: Common CRS (that I use)
EPSG:4326
  WGS84
  Lots of datasets are often given in this
  GPS coordinates
  Units: Decimal Degrees
EPSG:26910
  NAD83 | UTM zone 10
  Good enough for measuring area and distance locally here
  Units: meters
EPSG:3856
  Web maps (OSM, google)
  Basically same as 4326, but..
  Units: meters
UTM splits the earth into 60 segments, then in half again for north and south. Then fits a cylinder to the earth as shown, and unwraps the 3D surface into a 2D plane.
Just remember these magic EPSG numbers and that’s all you’ll probably need

## Slide 8: Vector Data

## Slide 9: Opening Vector Data in Python
Vector File types
  .shp Shape Files – ESRI ( ArcGIS )
  .json GeoJSON - Web
  .kml – KML - Google Earth
  Etc. – Many others
Python geospatial libraries (e.g., GeoPandas, Shapely, Fiona)
Typically I just use GeoPandas

## Slide 10: Data cleaning and preparation
Geospatial data often requires cleaning and preparation before analysis.
Common tasks include checking for missing or invalid data, transforming data to a common projection, and merging data from multiple sources.
This is like any other data source, and data processing step, nothing geospatial about it.

## Slide 11: Manipulating geospatial data
Geospatial data manipulation involves tasks such as spatial joins, buffering, overlays, and clipping.
Spatial joins involve combining data based on their spatial relationships, such as points within polygons or polygons intersecting with other polygons.
Buffering involves creating a distance around a point or line to represent a certain area of interest.
Overlays involve merging or intersecting two or more datasets to create a new dataset.
Clipping involves extracting a portion of a dataset based on a specified area of interest.
GeoPandas can handle all these tasks.

## Slide 12: Visualizing geospatial data
If it’s just for your own use:
Just load it into QGIS, way easier
If you need to make pretty interactive maps for stakeholders:
You can use libraries like Bokeh, and Altair for static maps, and Folium to create interactive maps.
Visualizing geospatial data can help reveal patterns, trends, and relationships that may not be apparent in tabular data.

## Slide 13: Raster Data

## Slide 14: Rasters are just Images
Contain meta data
  it stores the CRS the image is using, and the coordinates of the image in that reference frame.
Can Contain many color channels
  Not just Red, Green, Blue
  Near Infrared, Short Wave Infrared, Ultra blue
  https://gisgeography.com/sentinel-2-bands-combinations/

## Slide 15: How to analyse Rasters
Use Computer Vision
That’s beyond the scope of this talk though!
Then when you have detected stuff in the image, use the metadata in the image to convert the detected thing from image coordinates to earth coordinates

## Slide 16: NDWI for reservoir monitoring